Multimedia security and privacy
Section 2

---
(2.1) Explain the main differences between content fingerprinting (robust perceptual hashing) and cryptographic hashing
A cryptographic function has the following properties:
  - Noted: h(X) = y
  1. Input (X) is a binary string of any length (padding may be required)
  1. Output (y) is a binary string of a given length
  1. Changing a single bit in X, will change at least 50% of the bits of y
  1. From y, it is impossible to find the corresponding X
  1. It is computationally impossible to find collisions
  1. Some hashing functions may require the use of keys
Usage: Integrity
        (Authentication if key is used)

---
(2.1)
A content fingerprinting function has the following properties:
  - Noted: h(X) = bx
  1. Input (X) is a binary string of any length (N)
  1. Output (bx) is a binary string of a given length (L) => Short
  1. Changing a single bit in X, will have small repercussions on y => Invariant
  1. From y, it is impossible to find the corresponding X => Secure
  1. Easy to find collisions
  1. Some hashing functions may require the use of keys
Usage: Authentication and Identification

---
(2.1)
Levels of security
N >> L, since the hash is much smaller than the input data, it is impossible to recover X from bx. This also results in easy comparison between hashes.
Entropy of input: H(X) = N*H(Xi) = N*log2(256) = N*8
Entropy of output: H(bx) = L*H(bxi) = L*log2(2) = L*1 = L

---
(2.2) Explain the main usage of content fingerprinting in various applications. What are the main advantages?
Main Usages: authentication and identification
Authentication:
Example: a phone that is able to unlock via face recognition, must take a snap picture of a user (that wants to unlock the phone). The phone must decide “is it a verified user, or not?”
=> yes or no question

---
(2.2)
Identification:
Example: a phone keeps albums of images of each different person in its images. When taking a new picture, it needs to identify into which album the image must go.
=> Must decide which album, or none at all

---
(2.2)
Problems with doing these operations with the image itself:
Lets imagine we want to do both these operations with the image itself X
Let our image be of size N
In the authentication use case we need only to compare 2 images, each of size N => O(2*N) and O(N) (time/memory)
In the identification use case we need to compare to J albums (let’s assume each album has 1 image), every image of size N => O(J*N) and O(N*J) (time/memory)
Euclidean distance is a not a good measure of “likeness” in an image (not robust to geometrical operations)

---
(2.2)
If we instead compare the binary representation of each image bx, we get a certain number of advantages:
Speed and memory, as we can replace N by L (N >> L)
Vectors are binary, one can compute hamming distance instead of Euclidean distance
Secure in the event of data breaches (can’t recreate X from bx)
Robust to geometrical operations, compression
Follows known distribution (question 2.4)

---
(2.3) Explain the construction of content fingerprinting function based on random projections and binarization
Recall:
  - Noted: h(X) = bx
    1. Input (X) is a binary string of any length (N)
    1. Output (bx) is a binary string of a given length (L)

---
(2.3)
But what is h() doing exactly ?
  1. Vectorize input X
  1. Compute matrix W
  1. Compute:
  1. Turn into a 1 or a 0 (binarization)

---
(2.3)
Projection:
Binarization:

---
(2.3)
How do we compute matrix W ?
  1. There are 2 possibilities, it is either handcrafted (HC), or machine learning (ML)
HC uses a secret key k, that it uses as a seed to generate random values for W, whoever has access to the key k, can compute the same matrix W
ML uses machine learning algorithms to create the perfect matrix W, no key required

---
(2.3)
One question remains, which FP model is better ?
  - ML offers more robustness to geometrical operations/compression on X
  - ML needs training time to create a perfect encoder
  - ML is fully data dependant, meaning an attacker that has access to the data, can train his own model, and have a decoder
Both can be used, depending on the application one might be more appropriate!

---
(2.4) Explain the statistics of coefficients under random projections used in content fingerprinting. Properties.
  1. Vectorize input X
  1. Compute matrix W
  1. Compute:
  1. Turn into a 1 or a 0 (binarization)

---
(2.4)
It is impossible to know the statistical distribution of X
However it is very possible to know the statistical distribution of bx!
Let’s do it:
  - First of we have to understand that is statistically independent from , even though and are dependant, this is because the multiplication => , will make them independent
  - When we add multiple independent variables, the result is a gaussian of mean 0!
  - Because is gaussian of mean 0, it means that bx is of maximum entropy (if we choose the threshold correctly)!

---
(2.4)
  - Because and , we can compute the probability of error Pb, between two different binary strings
  - There are L independent events, and at each attempt there is a probability Pb of flip. This is a Binomial distribution!
  - From here we can compute expectancy and variance
  - With L large enough, our binomial distribution will be gaussian shaped (symmetrical). Which also means we can easily compute Pm and Pfa

---
(2.4)

---
(2.5) Explain the difference between the sufficient statistics in digital watermarking (linear cross correlation) and Hamming distance? What are the implications of these differences?
Linear cross correlation:
  - Used to detect the watermark in a media file
  - Block diagram:
  - Cross correlation used to answer yes/no
  1. Compute using
  1. Compute
  1. Compute
  1. Compute
  - If accept, the threshold

---
(2.5)
Hamming distance:
Used to decide if two FingerPrints are from close inputs
Hamming distance used to answer yes/no
Compute is any distortion
Compute
Compute
Compute
If accept, the threshold

---
(2.5)
Cross correlation result follows a gaussian distribution of mean
Hamming distance result follows a binomial distribution
if is large enough, is gaussian shaped!

---
(2.6) Explain the main requirements to privacy protection. Provide several examples of privacy protection schemes.